## Slide 1
How to Improve Usability of WCET tools
Dr.-Ing. Christian Ferdinand
AbsInt Angewandte Informatik GmbH

## Slide 2: The Timing Problem
Probability
Execution time
Exact worst-case execution time
Safe worst-case execution time estimate
Best-case execution time
Unsafe: execution time measurement

## Slide 3: aiT WCET Analyzer
The solution to the timing problem
Global program analysis
  abstract interpretation for cache, pipeline, and value analysis
  integer linear programming for path analysis
Everything combined in a single intuitive GUI

## Slide 4: aiT WCET Analyzer Structure
Loop trafo
CFG builder
Executable program
CRL file
Loop/value analyzer
Cache/pipeline analyzer
AIS file
CRL file
Static analyses
ILP generator
LP solver
Evaluation
Path analysis
WCET, visualization

## Slide 5: aiT WCET Analysis Input/Output
clock 10200 kHz ;
loop "_codebook" + 1 loop exactly 16 end ;
recursion "_fac" max 6;
SNIPPET "printf" IS NOT ANALYZED AND TAKES MAX 333 CYCLES;
flow "U_MOD" + 0xAC bytes / "U_MOD" + 0xC4 bytes is max 4;
area from 0x20 to 0x497 is read-only;
Specifications (*.ais)
Entry Point
Worst Case Execution Time
Visualization, Documentation
aiT
void Task (void)
{
variable++;
function();
next++:
if (next)
do this;
terminate()
}
Application Code
Executable (*.elf / *.out)
à =€@€ aŒ† | @€,@€;ÞKÿÿô;ÿ KÿÿØ‰€2}Œ`øÿÿ™€(8H#é³¡¶€(
Compiler Linker
Notes: Der StackAnalyzer ist ein Werkzeug, um den Stackbedarf einer Anwendung zu ermitteln. Diese Funktionalität bietet er jedem Anwendungs-Sourcecode.
Für osCAN wird er dahingehend erweitert, daß die Anforderungen eines preemptiven Betriebssystems berücksichtigt werden. Die für die einzelnen Tasks zu konfigurierenden Stackgrößen werden übersichtlich angezeigt.
Das Tool besitzt die einzigartige Eigenschaft, den Stackbedarf aus einer statischen Analyse des Anwendungsprogramms zu errechnen. Hervorzuheben ist, daß auch rekursive Vorgänge berücksichtigt werden.
Bei der Analyse wird der Aufrufbaum ermittelt. Als interessanter Nebeneffekt bietet dieses Werkzeug somit eine genaue Analyse der Softwarestruktur.

## Slide 6: Correctness of Pipeline Models Derivation of Pipeline Models from VHDL Specifications

## Slide 7: Integration into the Development Chain: SCADE / aiT automated Flow

## Slide 8: Integration into the Development Chain: Analysis Reports
Customizable HTML reports
Global and detailed reports
Diff feature

## Slide 9: Integration into the Development Chain: Scheduling Analysis Tools
System level: SymTA/S / RT-Druid
Code level: aiT/StackAnalyzer
System model (tasks, activation,scheduling)
WCET/stack analysis (single task)
Scheduling analysis (WCRT) system stack analysis
Refinement
WCET/stack request
WCET/stack response
Additional info

## Slide 10: Integration into the Development Chain: INTEREST Demonstrator: Engine Control System on TriCore 1796 (Ascet, SymTA/S, aiT)

## Slide 11: Exploration During Early Design Phases TimingExplorer
void Task (void)
{
variable++;
function();
while (next)
{
do this;
next--;
}
terminate();
}
Source files
 | 388 | 500 | 253
 | 760 | 896 | 543
T1
T2
WCET
T1

## Slide 12: Reduce the Amount of Annotations Source-Level Analyses
Source-level analyses to automatically generate AIS-annotations
  SWEET from Mälardalen University
  SATIRE from TU Vienna
    Upper bounds of loop iterations
    Targets of indirect function calls
    Mutually exclusive program part
Optimizing compilers require inspection of the binary code

## Slide 13: Reduce the Amount of Annotations Source-Level Analysis:Automatic Mode Detection
A mode of an application is usually characterized by the values of a set of variables
  The mode variables determine the control flow of the application
  The mode variables usually do not change during the execution
Source-level analysis to automatically detect application mode variables and values
  Implemented with SATIRE

## Slide 14: Summary
Safe deviation of pipeline models
Integrations with model-based development tools
Interface to scheduling analysis tools
Support to reduce the amount of annotations
New application areas
  Software integration
  Architecture exploration

## Slide 15: Research Projects

## Slide 16: Contact
www.absint.com
info@absint.com